## Slide 1
AEROTWIN OS
PRODUCT
From engine data to maintenance decisions
Product name: Frontend/src/app/components/Sidebar.tsx | October 2026
01
AeroTwin OS
Autonomous Predictive Maintenance
An integrated research prototype for health, remaining life, failure risk
and maintenance prioritization.
OVERALL PRODUCT / VERIFIED EVIDENCE / COMMERCIALIZATION
Notes: From engine data to maintenance decisions
Introduce AeroTwin OS as the name already used in the frontend. It is an integrated research prototype for aircraft-engine maintenance decision support. The objective is to give an engineer one traceable workflow from readings to recommended action. It is not deployed aircraft control or an approved maintenance authority. The supplied SharePoint template could not be retrieved; this is a standalone editable design.

## Slide 2
AEROTWIN OS
PRODUCT
The problem: signals do not equal decisions
Product problem hypothesis; to validate with maintenance teams
02
Fragmented evidence
Sensor trends, life estimates and
risk scores can point in different
directions.
Competing priorities
Early interventions consume
resources; late interventions can
disrupt operations.
Limited traceability
A recommendation needs a
reason, a confidence signal and
an engineer review path.
Product goal: turn separate predictions into a prioritized, explainable work queue.
Notes: The problem: signals do not equal decisions
These are the operational problems the product is designed to address, not measured customer findings. Maintenance teams need to reconcile sensor anomalies, life estimates, urgency and scheduling. Customer interviews and shadow pilots must validate their importance and the expected value.

## Slide 3
AEROTWIN OS
PRODUCT
One product, four connected components
Backend/main.py; Integration/routes.py; supervisor_bridge.py
03
01 RUL prediction
How much operating life remains?
02 Failure risk
How urgent is the risk over 10 / 30 / 50 cycles?
03 Health + anomalies
What changed, where, and why?
04 Maintenance supervisor
What should the team do next?
Unified output: a recommended action with priority, confidence and supporting evidence.
Notes: One product, four connected components
The four research components are implemented as two predictive services (RUL and failure risk), an anomaly and health service, and a maintenance supervisor. The shared FastAPI integration router orchestrates their existing implementations. Do not describe the rule-based combined pre-decision endpoint as the PPO supervisor; the real supervisor is invoked through the supervisor bridge.

## Slide 4
AEROTWIN OS
PRODUCT
Designed around the maintenance engineer
Frontend/src/app/pages; Frontend/src/app/routes.tsx
04
1
Upload
C-MAPSS .txt or
prepared .csv
2
Analyze
Validate and run the
four components
3
Review
Compare trends, risk
and explanations
4
Prioritize
Inspect the
supervisor work
queue
Feedback and review connect the recommended action to the engineer’s judgement.
Notes: Designed around the maintenance engineer
This is the implemented user journey supported by the Upload, Overview, RULPrediction, FailureRisk, HealthMonitoring, AIReasoning and MaintenanceSupervisor frontend pages. The UI reads backend results rather than recomputing predictive outputs in the browser. An engineer acts on the recommendation; no physical aircraft command is sent.

## Slide 5
AEROTWIN OS
PRODUCT
System architecture: evidence to action
Backend/app/services/Integration; Backend/main.py; Frontend/package.json
05
Data upload
Validate + route
RUL + uncertainty
→
Failure risk 10/30/50
→
Anomaly + health
→
Maintenance supervisor
PPO + policy guardrails
→
Operator dashboard
Queue, reasoning, feedback
↓
React + TypeScript UI | FastAPI services | Model artifacts + CSV/JSON exchange
Notes: System architecture: evidence to action
Source files: Backend/main.py mounts the component routers; Integration/feature_router.py routes the feature views; rul_failure_batch_service.py creates the RUL and failure-risk exchange CSVs; supervisor_bridge.py merges the upstream outputs and invokes the maintenance supervisor. Forecast inputs and frozen monitoring expectations are kept separate. React/TypeScript is the operator UI, with FastAPI/Python in the backend.

## Slide 6
AEROTWIN OS
PRODUCT
Evidence base: NASA C-MAPSS
Local C-MAPSS reader + forecast_target_080.json; NASA C-MAPSS documentation
06
4
C-MAPSS subsets
21
Sensor channels
3
Operating settings
Simulated engine trajectories; operating cycles are not hours.
Validation is retrospective. Real fleet data, maintenance outcomes and prospective testing are
still needed.
Notes: Evidence base: NASA C-MAPSS
The local reader supports FD001–FD004. Input rows contain engine identity, cycle, three operating settings and 21 sensor channels. NASA describes C-MAPSS as simulated turbofan engine data, so do not call this field validation. The reviewed official corpus contains 104,897 input rows and 707 engines. Forecast scoring covers 83,788 ready post-commissioning rows from 690 engines. See Backend/metrics/forecast_target_080.json for exact scoring masks and Backend/app/services/Anomaly_Health_Monitoring/Data_Preprocessing/cmapss_reader.py for parsing. NASA source: https://data.nasa.gov/dataset/c-mapss-aircraft-engine-simulator-data

## Slide 7
AEROTWIN OS
PRODUCT
RUL prediction: how much life remains?
Predictive_Maintenance/rul_lifecycle_service.py; saved evaluation_metrics.json
07
Implemented output
Temporal life estimate, degradation trajectory,
lifecycle state and prediction interval.
Where it helps
Supports inspection planning and highlights
accelerating or unstable degradation. Engineers
see the estimate alongside risk and health.
Saved pooled evaluation: R² 0.3954 | RMSE 37.69 cycles | 627 engines
Notes: RUL prediction: how much life remains?
The artifact loader searches per-subset TCN Keras artifacts and supporting scalers. Saved evaluation_metrics.json was generated on 24 August 2026. The deployed-path pooled evaluation uses the final observed window of 627 eligible official test engines; 80 engines are too short for the configured windows. RMSE is in cycles. R² varies considerably by subset. The interval coverage is empirical, not a blanket calibration guarantee. No RUL models were changed by the raw-sensor forecast improvement.

## Slide 8
AEROTWIN OS
PRODUCT
Failure risk: how urgent is the concern?
Failure_Risk FD002 metadata FINAL; failure_risk_service.py
08
Horizon
Decision context
Saved FD002 F1
Saved recall
10 cycles
Immediate attention
0.4800
0.5455
30 cycles
Near-term planning
0.7419
0.8846
50 cycles
Earlier preparation
0.8250
0.8462
BiLSTM prediction + uncertainty + calibrated thresholds; these figures are not all-subset metrics.
Notes: Failure risk: how urgent is the concern?
The failure-risk service loads per-subset BiLSTM artifacts and can use MC dropout for uncertainty. Horizons are operating cycles. Numerical values here are only FD002’s saved metadata, not fleet-wide accuracy: the official test engines were split 50/50 by a seeded permutation, thresholds were fitted on the calibration half, and these scores use the evaluation half. Thresholds were calibrated to prioritize recall where possible. A calibration recall target does not guarantee the same recall on new engines.

## Slide 9
AEROTWIN OS
PRODUCT
Health monitoring: explain the deviation
Anomaly_Health_Monitoring/config.py; ensemble_twin.py; verified forecast evaluation
09
Frozen monitoring reference
Context-aware healthy expectations drive
residuals, condition detection, health index and
subsystem reasoning.
Adaptive sensor forecast
Prior readings improve predictions of actual sensor
behavior. Forecast errors remain separate from
monitoring residuals.
Active raw-sensor forecast R²: 0.6417 → 0.6603. Frozen monitoring behavior is preserved.
Notes: Health monitoring: explain the deviation
The health pipeline models operating context, computes residuals from a frozen healthy reference, detects condition changes and generates subsystem explanations. Current config assigns anomaly fusion weight 1.0 to condition_consensus, with other detector weights at zero; do not describe all optional detectors as actively fused. The new adaptive raw-sensor forecast is a separate output using strictly prior sensor readings. It does not replace the frozen anomaly reference. Verification confirmed identical monitoring residuals, anomaly decisions and health indices on all 104,897 official inputs.

## Slide 10
AEROTWIN OS
PRODUCT
Supervisor: recommend the next action
Maintenance_Supervisor: champion manifest, decision_fusion, confidence, feedback
10
1
Continue
Operation
remains routine
2
Monitor
Increase attention
3
Inspect
Plan targeted
inspection
4
Maintain
Schedule
maintenance
5
Urgent
Immediate
maintenance
review
Inputs are fused with confidence, conflict checks and policy overrides before operator review.
Notes: Supervisor: recommend the next action
The champion manifest selects PPO. Decision fusion also applies explicit safety policy guardrails and confidence/conflict handling. The five actions are continue_operation, monitor_closely, schedule_inspection, schedule_maintenance and immediate_maintenance. These are software recommendations, not automatic aircraft shutdown controls. Feedback, explanation and counterfactual modules exist; counterfactual numerical changes should not be presented as physically validated control prescriptions.

## Slide 11
AEROTWIN OS
PRODUCT
Operator workspace: one view of the fleet
Frontend/src/app/routes.tsx; Overview.tsx; MaintenanceSupervisor.tsx
11
Fleet overview
Health state, RUL distribution, queue and drift
Engine investigation
Sensor traces, risk horizons and health history
Maintenance review
Action, priority, confidence and explanation
Evidence + feedback
Reports, model metrics and engineer response
Schematic of implemented UI capabilities; each view reads backend outputs.
Notes: Operator workspace: one view of the fleet
This is a schematic feature map of implemented frontend pages, not a screenshot or a claim of live production deployment. Overview includes fleet summaries, maintenance queue and drift context. Other routes expose RUL, failure risk, health, anomaly, digital twin, AI reasoning, confidence, reports and settings. Supported backend integration and artifact availability determine what can be displayed.

## Slide 12
AEROTWIN OS
PRODUCT
Measured results: keep the metrics distinct
forecast_target_080.json; Predictive_Maintenance/evaluation_metrics.json
12
Evaluation
Before
Active / saved result
Raw-sensor forecast R²
0.6417
0.6603
Raw-sensor RMSE
0.4318
0.4205
Raw-sensor MAE
0.2482
0.2383
RUL prediction (pooled)
Separate task
R² 0.3954; RMSE 37.69 cycles
The requested official raw-sensor R² of 0.8 has not been reached.
Notes: Measured results: keep the metrics distinct
Raw-sensor values are the new active forecast on the reused official full-trajectory benchmark: 83,788 ready rows, 690 engines. R² is the unchanged mean over informative channels; RMSE and MAE include all 21 normalized raw targets. The healthy-only metric is a separate population and is 0.565393, not the full-trajectory score. Confirmation full-trajectory R² is 0.798732 on a different previously inspected cohort and does not establish official R² 0.8. RUL evaluation is a separate task and cannot be substituted for sensor R². All figures come from saved artifacts, not a new all-product evaluation run.

## Slide 13
AEROTWIN OS
PRODUCT
Supervisor economics: simulation evidence
Saved policy_evaluation_report.json | 28 simulated test episodes
13
28
Offline test engines
0 / 28
Simulated failures
78.98%
Simulated cost reduction
Comparison: reactive baseline. Rule-based policy also had zero simulated failures.
Simulation outcomes depend on assumed costs and downtime; customer ROI is not validated.
Notes: Supervisor economics: simulation evidence
Source: Backend/reports/Maintenance_Supervisor/policy_evaluation_report.json. The saved report evaluates 28 held-out run-to-failure engines in an offline policy simulator. Champion observed zero catastrophic simulated failures, compared with nine for reactive_tbo_baseline. Rule cascade also had zero failures, so PPO does not demonstrate a safety improvement over that baseline. Cost reduction 78.98% and downtime reduction 68.89% are conditional on simulator action costs and event downtime assumptions. They are not airline savings or field safety evidence. Example action costs include $30 monitoring, $150 inspection, $500 scheduled maintenance and $1,200 immediate maintenance.

## Slide 14
AEROTWIN OS
PRODUCT
What is validated, and what still needs work
Forecast verification + saved RUL evaluation; production roadmap proposals
14
Verified in the local project
150 forecast/regression tests pass.
Normal retraining reproduces the candidate.
Monitoring outputs remain unchanged.
Before operational adoption
Improve multi-condition RUL accuracy and interval
calibration. Validate real fleet data, alert burden and
workflow integration.
Current maturity: integrated research prototype, ready for a controlled advisory pilot.
Notes: What is validated, and what still needs work
The 150 passing tests cover the forecast and related anomaly/health regression suite, not the entire product. The forecast retraining audit reproduces 16,808 development trajectory predictions and confirms the selected training plan and forecast role. Monitoring invariance was verified on 104,897 official inputs. Saved RUL interval coverage PICP is 0.5518 on its pooled endpoint evaluation, so the product cannot claim uniformly calibrated nominal coverage. FD002/FD004 RUL errors are substantially larger than FD001/FD003. Real-fleet transportability, security and operational integration remain pilot work.

## Slide 15
AEROTWIN OS
PRODUCT
From prototype to a deployable pilot
Gap analysis from repository implementation; proposed roadmap
15
Data + model readiness
Prospective holdout data, sensor
mapping, missing-data tests,
calibration and drift checks.
Operational readiness
Authentication, audit logging,
monitoring, deployment
packaging and measured
latency.
Workflow readiness
Engineer approval, maintenance
records, work-order integration
and accountable ownership.
Pilot release gate: evidence quality + workflow safety + reproducible deployment.
Notes: From prototype to a deployable pilot
This is a proposed engineering roadmap, not a list of completed security or enterprise integrations. First validate the data contract and deploy in an isolated environment. Then add authentication, access control, secrets management, audit trails, monitoring and CI/CD. CMMS/work-order integration, procurement requirements and aviation assurance need a partner-specific plan. Human approval remains mandatory in the proposed commercial advisory workflow. Forecast latency increased in one 104,897-row audit from 124.61 to 201.29 seconds; optimize throughput and measure target-hardware latency before a live-service commitment.

## Slide 16
AEROTWIN OS
PRODUCT
Evidence used in this presentation
Full paths and external references are included in speaker notes and the companion notes file
16
Implementation
FastAPI integration + four component services
React / TypeScript operator workspace
Measured evidence
Locked forecast evaluation; saved RUL metrics; FD002 risk metadata; offline supervisor policy
evaluation.
External context: NASA C-MAPSS / IBM Maximo APM / Airbus Skywise
Notes: Evidence used in this presentation
Internal sources are relative to the repository root: Backend/metrics/forecast_target_080.json; Backend/experiments/Anomaly_Health_Monitoring/run_20261016_forecast_080/verified_evaluation.json; Backend/metrics/Predictive_Maintenance/evaluation_metrics.json; Backend/models/Predictive_Maintenance/Failure_Risk/FD002_bilstm_failure_risk_metadata_FINAL.json; Backend/reports/Maintenance_Supervisor/policy_evaluation_report.json; Backend/app/services/Integration; Frontend/src/app/pages. External product pages were checked in October 2026: NASA https://data.nasa.gov/dataset/c-mapss-aircraft-engine-simulator-data ; IBM https://www.ibm.com/products/maximo/asset-performance-management ; Airbus https://www.airbus.com/en/newsroom/news/2017-06-skywise-airline-early-adopter-highlights . The public NASA page describes simulator provenance; channel counts come from the local reader. Competitor product descriptions support positioning only, not a head-to-head benchmark.

## Slide 17
AEROTWIN OS
COMMERCIALIZATION · 1 / 5
Commercialization: start with one buyer
Proposed positioning; official IBM Maximo APM and Airbus Skywise descriptions
17
Initial buyer
MRO or fleet reliability manager with usable
engine data, a defined triage problem and an
engineer champion.
Initial offer
A bounded advisory pilot: one fleet or asset
group, one workflow, one baseline and clearly
measured outcomes.
Positioning hypothesis: explainable maintenance triage with a practical integration path.
Notes: Commercialization: start with one buyer
Proposed beachhead: one independent maintenance, repair and overhaul organization or airline reliability team with historical data and an accountable engineer sponsor. No customer, partnership or willingness-to-pay evidence is currently established. Airbus already offers Skywise predictive maintenance and IBM Maximo APM provides enterprise health and predictive workflows. AeroTwin OS should be positioned as a focused advisory pilot, not as the first unified maintenance system or a certified substitute. Local/regional outreach can be tested, but no market size estimate has been invented.

## Slide 18
AEROTWIN OS
COMMERCIALIZATION · 2 / 5
Commercial offer and proposed pricing
Proposed business assumptions; validate before quoting customers
18
Paid pilot
8–12 weeks
$5k–$15k
Data audit, shadow
evaluation and evidence
report.
Subscription hypothesis
$1,000/site/month
+ $20/engine/month
50 engines: $24k annual
recurring revenue.
Enterprise options
Partner-specific quote for
private hosting, integrations,
support and assurance work.
Pricing is illustrative USD; no customers, revenue or willingness to pay are claimed.
Notes: Commercial offer and proposed pricing
All prices are proposed USD assumptions to test in buyer interviews, not a market quote, existing contract or validated willingness to pay. Pilot: $5,000–$15,000 for 8–12 weeks including data assessment and a pilot report. Subscription hypothesis: $1,000 per site/month plus $20 per monitored engine/month. At 50 engines that is $2,000/month or $24,000/year before taxes, bespoke integrations and support. A $10,000 setup assumption is used in the following ROI example. Enterprise terms would depend on data hosting, support, connectors and assurance requirements. No prices are based on competitor pricing.

## Slide 19
AEROTWIN OS
COMMERCIALIZATION · 3 / 5
Go to market through evidence, then expand
Proposed 12-month launch plan; milestones are targets
19
Months 0–3
Interview users.
Secure one design partner.
Agree scope, baseline, data
access and review criteria.
Months 3–6
Run an advisory shadow pilot.
Measure lead time, alert burden
and planner effort.
Review every intervention.
Months 6–12
Convert if the pilot passes.
Package repeatable
onboarding.
Test with two further partners.
Pilot exit: prospective evidence, engineer acceptance, buyer approval and a viable delivery cost.
Notes: Go to market through evidence, then expand
Illustrative first-year plan. Months 0–3: interview around ten prospective users, secure one design partner and agree data access, sponsor and baseline. Months 3–6: conduct an 8–12 week shadow pilot; engineers keep authority, measure alerts per 100 operating cycles, actionable alert fraction, lead time, planner effort and independently reviewed intervention opportunities. Compare against the partner’s current process on prospective data. Months 6–12: seek a paid conversion only if the agreed operational, data, security and economic gates pass; then test repeatability with up to two additional partners. These are targets, not existing achievements or guaranteed sales.

## Slide 20
AEROTWIN OS
COMMERCIALIZATION · 4 / 5
Customer ROI: an explicit testable model
Illustrative assumptions only; replace every input with customer-validated values
20
Illustrative first-year input
Calculation
Value
Avoided disruption value
2 × $25,000
$50,000
Planner time value
200 hours × $50
$10,000
Subscription + setup
$24,000 + $10,000
$34,000
Net benefit / modeled ROI
$60,000 − $34,000
$26,000 / 76.5%
Without verified avoided events, this example loses $24k in year one. Validate attribution.
Notes: Customer ROI: an explicit testable model
This is an illustrative business case, not a claim of measured airline economics. Annual gross benefit = independently verified avoided-event value + planner hours saved × loaded hourly value. Assumptions: two avoided disruption events/year at $25,000 each plus 200 planner hours/year at $50/hour give $60,000. First-year cost is $24,000 subscription for 50 engines plus $10,000 setup, total $34,000. Net modeled benefit $26,000. First-year ROI is ($60,000−$34,000)/$34,000 = 76.47%. Attribution of avoided events is difficult and must be agreed before a pilot, with independent review to avoid crediting events that would not occur. Sensitivity: with zero verified avoided events and only $10,000 labor benefit, the first-year net benefit is negative $24,000. Simulator cost savings are not used as customer ROI inputs.

## Slide 21
AEROTWIN OS
COMMERCIALIZATION · 5 / 5
Commercialization plan: earn the right to scale
Proposed commercialization actions; ownership, budget and customer evidence still to secure
21
1 Secure the partner
One scoped buyer problem,
usable historical data, engineer
sponsor and a paid pilot
agreement.
2 Prove operational value
Prospective evaluation,
reviewed actions, acceptable
alert burden, security checks
and auditable ROI.
3 Scale a repeatable offer
Convert the pilot, standardize
onboarding and support, then
expand to additional fleets.
Next milestone: one paid design-partner pilot with success and stop criteria agreed in advance.
Notes: Commercialization plan: earn the right to scale
End with a practical commercialization ask, not a claim that research metrics prove product-market fit. Secure one design partner and one operational owner; define advisory use and human review; budget engineering, data integration and domain expertise; approve no-go criteria and measured ROI before expanding. Required roles are an ML/backend engineer, a frontend/integration engineer and a domain maintenance sponsor, with security and commercial support as needed. Initial distribution is founder-led/direct partner outreach and a case study with permission. Longer-term channels could include systems integrators or CMMS partners, but no such partnerships exist yet. The objective is a repeatable paid workflow with trusted evidence, not a nominal R² threshold alone.